## Slide 1: RCA (Root Cause Analysis)
Traditional Model Based
  System models: Cluster, Network switches and links, and Client
  Fault tree
  Evidence data trace:
    Symptoms -> system components
Machine Learning
  Monitoring data time series: pattern or distribution changes
  Log files: text mining
  Tomography inference
Probabilistic :
  Bayesian Network
Deterministic :
  SVM
  Decision Tree
  Neural Net
System Models
Data
RCA Reasoning
RCA Model

## Slide 2
Flow 1 path : uc-submit, link 18, link12, link 1, link22, link 23, ucsd-compute—c3
Flow 2 path : syr-compute-c2, link 26, link 24, link 7, link22, link 23, ucsd-compute—c3
Flow 3 path : uc-stage, link 19, link 12, link 1, link22, link 23, ucsd-compute—c3

## Slide 3: RCA (Root Cause Analysis)
Learning what?
  Infer node/link labels (classes) from end-to-end flow-level monitoring
  What-IF
Flow 1
uc-submit
Labels
Flows
link 18
link12
link 1
link22
link 23
ucsd-compute—c3
link 19
syr-compute-c2
link 26
link 24
Flow 2
Flow 3
link 7
uc-stage
  F2 observed corruption
  F1 observed corruption
  F3 observed corruption
  F2 observed corruption
  F3 observed corruption
Y
N
Y
N
Labels/classes

## Slide 4: RCA (Root Cause Analysis)
Learning what?
  Topology unknown and Routes unknown
  Infer node/link labels (classes) from end-to-end flow-level monitoring
F1
F2
Fi
Fn-1
Fn
L1
L2
Lj
Lk-1
Lk
.
.
.
.
.
.
.
.
.
.
.
.
Flows
Links/Nodes
Flow 1
uc-submit
Labels
Flows
link 18
link12
link 1
link22
link 23
ucsd-compute—c3
link 19
syr-compute-c2
link 26
link 24
Flow 2
Flow 3
link 7
uc-stage
?

## Slide 5: Literature
007 (Azure, 2018) | 
TCP retransmission | Path -> Link loss ranking
PingMesh (2015) |  | 
Packet Latency | Link Latency and Loss, Server and software latency | Ping measurement, Manual analysis
Failure (KDD 2014) | 
IP Packet | Link loss ranking
NetBouncer (NSDI 2019) | 
IP Packet | Link loss
NetPoirot (SigCom’16 ) | 
TCP | Network or server
Detector (ATC’17) |  | 
Packet loss, routing Matrix | Link coverage, Identifiability | Efficient probe path Link rank
DiagNet (2020) | 
TCP, HTPP Client Measurement | Internet location performance
NetScope (2010) | 
IP packet | Link loss
Y
TCP and IP level RCA: Solved problem, matter of bigger scales
Matter of measurement coverage
numerical features + known routing
RCA: Incomplete info + bigger scale:
mixed (continuous + categorical) features + unknown topology/routing

## Slide 6: Design Space
Failure mode | 
Hard failure | Gray Failure
Topology information | 
Complete | Incomplete
Flow Routing | 
Complete | Unknown
Monitoring | 
Active Probe | Passive monitoring
Fault | 
Passive monitoring | Injection
System | 
Production | Emulation
Flows | 
All Node Pair | End Hosts Only

## Slide 7: Emulation Experiments in ExoGENI (Small)

## Slide 9: OSG Topology

## Slide 10: IRIS ML Approach
Combined workflow and incomplete infrastructure features
  Inference from end-to-end flow integrity checks
  Training data generation from fault injection
Cast it as a network system RCA problem using ML approach
  Decision Tree
  SVM
  NN

## Slide 11: Emulation of a smaller OSG Network
I2
Data Origin Sites
Control Host
OSG Site 2
s1
c1
c3
c2
OSG Site 1
Network
d1
N1
N3
N2
N4
N5
N6
d2
d3
d4
s2
G(V, E) = G((C,N,S,D), E)
Routes unknown

## Slide 12: Bigger OSG network : automation
1. Experiment automation:
  Postboot script
  OSPF Configuration
2. Fault injection and Data Collection Automation
  ChaoJungle injection on both router and host nodes
  Data collection
3. Analysis and ML modeling in Jupyter